Controlling the world with Ruby
AKA “8-bit stuff”
Paul Grayson
Las Vegas Ruby User Group
2015-01-21

---
Thinking outside the box

---
Controlling physical devices
- Need to build circuitry
- Precise timing requirements (microseconds)
- Variety of interfaces

---
CPUs aren't good at that
- Not easy to wire up to things
- Unpredictable timing - milliseconds
- Few low-level interfaces

---
Microcontrollers!
- Available in hacker-friendly packages
- Precise sub-microsecond timing
- Many interfaces, timers, ADC, etc.
- Typically 8-bit / 32k program / 2k RAM

---
Solution: microcontroller + CPU
?
- Serial (RS-232)
- I2C
- Audio
- USB

---
USB virtual serial port
Bytes sent and received on /dev/ttyACM*, /dev/cu.usbmodem*, COM*

---
LED demo
RGB 5-bit color = 15 bits/pixel
byte 1 byte 0
0rrrrrgg gggbbbbb

---
Bit operators in Ruby
- &, |, ^ - AND, OR, XOR
- <<, >> - left, right shift
  0bxxxxxxxx << 3 = 0bxxx_xxxxx000
  0bxxxxxxxx >> 3 = 0b000xxxxx
  0rrrrrgg gggbbbbb =
  (r << 10) + (g << 5) + b
  better: ((r & 31) << 10) + ...